## Slide 1: Greenhouse digital TWIN
Ioannis Tsampras ioannis.tsampras@upnet.gr
Stavros Kanias up1066584@upnet.gr

## Slide 2: Contents
The Project
Goals & System Design
Architecture - Technologies
The Inner Workings
Deployed Demo
Our Work / Timetable

## Slide 3: The project
A Device, Cloud and Processing infrastructure for distributed digital twins of herbaceous plant type greenhouses.
Taking advantage of dwindling power and hardware cost for edge data ingestion we implement an AI solution in top-view image mapping and detection along with a distributed database cloud solution.
Our cable-lift low cost and easy installation robot moves through the length of a greenhouse, takes top-down images and in real time maps it’s position while detecting individual plants, saving multiple snapshots for each and forwarding metrics & sensor data to the cloud.
…..

## Slide 4: PRIMARY GOALS
Low cellular data usage
Inexpensive hardware & installation
Full digital representation
Optimization Axes
ARCHITECTURAL CHOICES
System Design
Mapping and detection on edge (cost, data usage)
Metrics extraction on site , updating central Db only for metrics (data usage)
On demand access to media through distributed Db, central Db cache (data usage)
MQTT front view refresher
LAN option for data extraction (data usage)

## Slide 5: SOFTWARE Architecture
Front View
Server
(back-end)
Front View
. . .
MQTT Broker
Publish
Subscribe
Serve Pages
Central Db
Edge API Controller
. . .
Edge API Controller
Request Media
Update Database
Data Ingestor
Distr. Db
Sys Call
Simulation or Environment

## Slide 6: DEVICE FLOW DIAGRAM
GPIO PINS
Internet
Dev Board
Motor & Driver
Camera
Sensor
Sensor
Sensor
Environmental Sensors (Temp, Humidity, CO2 and more)
USB
Access point
LAN
LAN
Server
Central Db
MQTT Broker
Front View
Mail Service

## Slide 7: The INNER WORKINGS​
Total Position
Curve Finder
Curve Finder
Curve Finder
Thresholding on GB
Sum of Vertical Scan
FFT smoothing & Normalization
Crop
Edge Filter Thresholding
Explorative low cost clustering
abs[(log(abs(f’(x)))’]
Compare to History with Σ(Δy )
2
Translate
Attach
FFT smoothing & Normalization
High Accuracy Clustering where N-clusters = k-max
Centers
Lines & limits
Offset
Local Indexes
Store
snapshots

## Slide 8: LIVE DEMO
…

## Slide 9: TIMELINE
Image Detection AI
Edge Controller API
Mapping System
Simulation
Hardware & Deployment
Webpage Draft
Database &
Server
Edge API Integration
Log-in & Visualization
MQTT Front View

## Slide 10: THANK YOU
Ioannis Tsampras & Stavros Kanias
www.github.com/Skorpinakos/IoT-2022